## Slide 1
Smartphone Based Detection of Retinal Abnormalities
Rohaid Ahmed Mirza
Shakir Khan
M. Zain Zubair
FA19-BCE-006
FA19-BCE-008
FA19-BCE-027
COMSATS University Islamabad
Department of Electrical and Computer Engineering
Supervised By
Dr. Syed Saud Naqvi
Associate Professor
Dr. Haroon Ahmed Khan
Assistant Professor

## Slide 2
Agenda
Introduction
Block Diagram
Bibliography
Literature Review
Project Description
Notes: Image by freepik

## Slide 3
Introduction
People with Diabetes develop Diabetic Retinopathy (DR) that may lead to vision loss.
One of its early indicators is changes in retinal blood vessels’ structure.
DR is the leading cause of new cases of blindness in people with diabetes. [1]
In Pakistan, 27.4 million people above the age of 20 are affected by diabetes. [2]
[1] https://www.cdc.gov/visionhealth/pdf/factsheet.pdf
[2] Basit A, Fawwad A, Qureshi H NDSP Members, et al Prevalence of diabetes, pre-diabetes and associated risk factors: second National Diabetes Survey of Pakistan (NDSP), 2016–2017BMJ Open 2018;8:e020961. doi: 10.1136/bmjopen-2017-020961
Notes: 27.4 million people over the age of 20 (26.3% of this age group) are affected by diabetes – four times higher than in the 1998 survey.
(the light-sensitive layer of tissue in the back of your eye).

## Slide 4
Introduction
Diagnosis of DR from Fundus images is typically done by large, unportable and expensive equipment
You need trained clinical specialists (ophthalmologists) to operate these types of equipment
There is a huge disparity between availability of equipment and specialists versus the number of patients
Notes: Image by freepik

## Slide 5
Introduction
Diagnosis of DR from Fundus images is typically done by large, unportable and expensive equipment
You need trained clinical specialists (ophthalmologists) to operate these types of equipment
There is a huge disparity between availability of equipment and specialists versus the number of patients
A lot of current research is being carried out to automate this process without the equipment and the specialist
Notes: Image by freepik

## Slide 6
Introduction
Automation reduces the manual errors and increases the efficiency of the system.
Automation on mobile makes the model/system portable to use anywhere anytime .
The goal is to take the automatic detection algorithm to the palm of hand.
Notes: Image by freepik

## Slide 7
Literature review
Research | Contributions
Detection of retinal abnormalities using Smartphone-captured fundus images: A survey (Mohamed Akil, Yaroub Elloumi) [3] | This study in enclose by a discussion where we report the requirement of normalized approach for fundus image capture, a well-defined preprocessing to fundus image enhancement and the implementation of machine learning on Smartphone to insure a local detection.
Comparison of smartphone-based retinal imaging systems for diabetic retinopathy detection using deep learning (Mahmut Karakaya & Recep E. Hacisoftaoglu ) [4] | This paper investigated the smartphone-based portable retinal imaging systems, namely iExaminer, D-Eye, Peek Retina, and iNview to compare their image quality.
[3] Mohamed Akil, Yaroub Elloumi. Detection of retinal abnormalities using Smartphone-captured fundus images: A survey. Real-Time Image Processing and Deep Learning, Apr 2019, Baltimore, Maryland, United States. ff10.1117/12.2519094ff. ffhal-02121855f
[4] Karakaya, M., Hacisoftaoglu, R.E. Comparison of smartphone-based retinal imaging systems for diabetic retinopathy detection using deep learning. BMC Bioinformatics 21 (Suppl 4), 259 (2020). https://doi.org/10.1186/s12859-020-03587-2

## Slide 8
Literature review
Research | Contributions
CABnet: Category Attention Block for Imbalanced Diabetic retinopathy Grading (Along He, Tao Li , Ning Li, Kai Wang) [5] | CABNet combines category attention block (CAB) and global attention block (GAB). CABNet can be trained in an end-to-end manner for fine-grained DR grading and learn discriminative features by the attention module.
Comparison of automated and expert human grading of diabetic retinopathy using smartphone-based retinal photography (Tyson N. Kim, et al.) [6] | A smartphone-based camera was used by non-ophthalmic personnel to image the retina of diabetic patients. Images were independently evaluated by two masked readers and categorized as refer/no refer
[5] He, A., Li, T., Li, N., Wang, K. and Fu, H., 2020. CABNet: category attention block for imbalanced diabetic retinopathy grading. IEEE Transactions on Medical Imaging, 40(1), pp.143-153.
[6] Kim, T.N., Aaberg, M.T., Li, P. et al. Comparison of automated and expert human grading of diabetic retinopathy using smartphone-based retinal photography. Eye 35, 334–342 (2021). https://doi.org/10.1038/s41433-020-0849-5

## Slide 9
Problem Statement
Cost
Bear:
  Medical specialist expense
  Visit frequency
Misdiagnosis
Due to:
  Lack of training or expertise of the ophthalmologist
  Malpractice

## Slide 10
Proposed Solution
Automated Analysis
Captured image would be analyzed automatically by the mobile application.
Grading
The grading of the model would tell whether the level of pathology is referable to ophthalmologists or not.
Cost Saving
Doctor appointments’ fee and commute cost for every visit would be saved.
Smartphone in the pocket would replace the expensive fundus imaging cameras.

## Slide 11
Project Description

## Slide 12: Block Diagram Smartphone Application
Output
Recognition
Diagnosis
Smart Phone
DR
Application
Smart Phone Camera/Gallery
Retinal Image
Server
Notes: Image by freepik

## Slide 13: Block Diagram Web Application
Computer
DR Web
Application
File Explorer
Retinal Image
Server
Output
Recognition
Diagnosis
Notes: Image by freepik

## Slide 14: Flow Chart
Image Acquisition
Server
Network
Model 1
Application
Outcome
If retinal?
Server
Network
Model 2
Image
True (Retinal)
Referable/Non-Referable
False (Non-Retinal)
Retinal/Non-Retinal
Image
Notes: Image by freepik

## Slide 15: Process Flow Diagram
DR Detection
Image Acquisition
Model Training
Model Training
Model Testing
Image Preprocessing
Resize
Augmentation
Noise Removal
Analysis
Accuracy
Specificity
Sensitivity
Notes: Image by freepik

## Slide 16: Artificial Neural Networks; Image Classifiers
Machine learning model inspired by the human brain's neural network structure.
Effective in image classification; ability to learn complex patterns and relationships within the data.
Can automatically extract relevant features from images, recognize and classify objects or patterns in images accurately
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 17: Convolutional Neural Networks (CNN) over Simple ANN
Specialized type of ANN specifically designed for image processing and recognition tasks
Unique architectural elements such as convolutional layers, pooling layers, and fully connected layers
Optimized for image processing tasks, with improved performance and accuracy over simple ANN architectures
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 18: Convolutional Neural Networks (CNN) over Simple ANN
Convolutional layers; apply filters, extract features from images preserving their spatial relationships
Pooling layers reduce the spatial dimensions of feature maps, enabling model to be invariant to small changes
Parameter and weight sharing across convolutional layers, learning spatial hierarchies of features efficiently
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 19: Convolutional Neural Networks (CNN) over Simple ANN
Convolutional layers; apply filters, extract features from images preserving their spatial relationships
Pooling layers reduce the spatial dimensions of feature maps, enabling model to be invariant to small changes
Parameter and weight sharing across convolutional layers, learning spatial hierarchies of features efficiently
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 20: Classification Networks
Two networks trained for the project
  Network 1; Retinal Image Identification
    One of the Two models proposed to be used; simple ANN or Mobilenetv2
    No/less complex patterns to be detected
  Network 2; DR Detection
    Complex patterns to be trained on
    MobileNetv2 used
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 21: Network 1: Retinal Image Identification
Goal: Develop a classification model to identify between retinal images.
Dataset: Two classes - "non-retinal" (real-world images) and "retinal" (retinal images).
Training: Simple artificial neural network (ANN) architecture.
Alternative Approach: MobileNetV2 due to limitations on complex features.
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 22: Network 2: DR Detection
Objective: Detect DR in retinal images
Training: Deep learning model trained on 18,000 retinal images from the EyePacs dataset
Classes: "Referable/DR" and "Non-Referable/No-DR" for disease classification
Knowledge Transfer: fine tuning on DDR dataset
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 23: Dataset Acquisition
A dataset consisting of real-world images, including non retinal images, was used.
  The dataset of random images was sourced from Kaggle.
Two datasets for retinal images:
  EyePacs dataset;
    Taken from “Kaggle Diabetic Retinopathy Detection Competition. Accessed: Apr. 11, 2020. [Online]”
    Around 35000 retinal images
  DDR dataset;
    Taken from “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” by T. Li et. al. [7]
    Around 12000 retinal images
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Notes: Image by freepik

## Slide 24: Dataset Acquisition
One data set for real-world images say non retinal
  Random images dataset; Taken from kaggle
Two datasets for retinal images:
  EyePACS dataset;
    taken from “Kaggle Diabetic Retinopathy Detection Competition. Accessed: Apr. 11, 2020. [Online]”
    Around 35000 retinal images
  DDR dataset;
    taken from “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” by T. Li et. al. [7]
    around 12000 retinal images
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Label | Grading Name
0 | No DR
1 | Mild DR
2 | Moderate DR
3 | Severe DR
4 | Proliferative DR
Notes: Image by freepik

## Slide 25: Dataset Acquisition
One data set for real-world images say non retinal
  Random images dataset; Taken from kaggle
Two datasets for retinal images:
  EyePACS dataset;
    taken from “Kaggle Diabetic Retinopathy Detection Competition. Accessed: Apr. 11, 2020. [Online]”
    Around 35000 retinal images
  DDR dataset;
    taken from “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” by T. Li et. al. [7]
    around 12000 retinal images
[7] T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
Label | Grading Name
0 | No DR
1 | Mild DR
2 | Moderate DR
3 | Severe DR
4 | Proliferative DR
a
b
c
d
e
(a) No DR; (b) Mild DR; (c) Moderative DR; (d) Severe DR; (e) Proliferative DR;
Notes: Image by freepik

## Slide 26: Data Preparing
Both models trained for two classes
Original datasets to be prepared according to required tasks:
  Network 1 for retinal image identification
    Non retinal images include random real-world images
    Retinal images
  Network 2 for DR detection
    Non-Referable refer to no DR
    Referable refer to DR
Network Models | Label
Network Model 1 | Non-Retinal
1 | Retinal
Network Models | Label
Network Model 2 | Non-Referable (No DR)
1 | Referable (DR)
Notes: Image by freepik

## Slide 27: Image Pre-processing
Developed by former Kaggle competition winner Ben’s Graham
Used for DR detection
Crop dark regions and resize image
Notes: Image by freepik

## Slide 28: Bens Graham Preprocessing Technique
combines the original image and its Gaussian blur
enhance edges and features
[8] Wang S, Zheng J, Hu HM, Li B. Naturalness preserved enhancement algorithm for non-uniform illumination images. IEEE Trans Image Process. 2013 Sep;22(9):3538-48. doi: 10.1109/TIP.2013.2261309. Epub 2013 May 2. PMID: 23661319.
Figure: Images Before and After Applying Ben Graham's Preprocessing
Notes: Image by freepik

## Slide 29: Model Training
Preprocessing complete
Data trained on the following model using TensorFlow:
  MobilenetV2
MobileNetV2; a popular convolutional neural network (CNN) architecture
designed for efficient computation on smartphones
lightweight model, achieves high accuracy
Minimizes computational resources and memory footprint.
Offers a good balance between model size, inference speed, and accuracy,
Notes: Image by freepik

## Slide 30: Model Training
Preprocessing complete
Data trained on the following models using TensorFlow:
  MobilenetV2; both tasks
  Simple ANN; retinal image identification
Notes: Image by freepik

## Slide 31: Model Training
Preprocessing complete
Data trained on the following models using TensorFlow:
  MobilenetV2; both tasks
  Simple ANN; retinal image identification
Notes: Image by freepik

## Slide 32: Model Training
MobileNetv2; a popular convolutional neural network (CNN) architecture
Designed for efficient computation on smartphones
Lightweight model, achieves high accuracy
Minimizes computational resources and memory footprint.
Offers a good balance between model size, inference speed, and accuracy,
Notes: Image by freepik

## Slide 33: Network 1 Model Training
The model is trained on ANN architecture
Accuracy and loss for retinal image identification
Notes: Image by freepik

## Slide 34: Network 1 Model Training
The model is trained on ANN architecture
Accuracy and loss for retinal image identification
 | Precision | Recall | F1-Score | Support
Non-Retinal Image | 1.0 | 1.0 | 1.0 | 2340
Retinal image | 1.0 | 1.0 | 1.0 | 2405
Accuracy |  |  | 1.0 | 4745
Notes: Image by freepik

## Slide 35: Network 1 Model Training
The model is trained on MobileNetV2
Accuracy and loss for retinal image identification
Notes: Image by freepik

## Slide 36: Network 1 Model Training
The model is trained on MobileNetV2
Accuracy and loss for retinal image identification
 | Precision | Recall | F1-Score | Support
Non-Retinal Image | 1.0 | 1.0 | 1.0 | 2340
Retinal image | 1.0 | 1.0 | 1.0 | 2405
Accuracy |  |  | 1.0 | 4745
Notes: Image by freepik

## Slide 37: Network 1 Model Training
MobileNetV2 model demonstrates superior performance
MobileNetV2 chosen over the simple ANN architecture
Notes: Image by freepik

## Slide 38: Network 2 Model Training
Accuracy and loss for DR detection.
Trained on EyePacs dataset.
Applied Ben’s Graham Preprocessing Technique.
Validated on DDR dataset.
Without fine tuning
Notes: Image by freepik

## Slide 39: Model Training
Accuracy and loss for DR detection
Trained on EyePACS
Without fine tuning on DDR
Network 2 Fine Tuning Model
Accuracy and loss for DR detection.
Applied Ben’s Graham Preprocessing Technique.
Fine tuned on DDR dataset.
Notes: Image by freepik

## Slide 40: API Generation
Python framework
For API generation
Model deployed on server
API is used for communication with server
Flask:
Notes: Image by freepik

## Slide 41: Model Deployment
Python code written with flask framework
Pushed to server
API generated by server and flask
Application communicate with server using API
Notes: Image by freepik

## Slide 42: Mobile Application
Mobile application for the project is developed on Flutter framework.
Dart as programming language
Designed to maintain UI design uniformity across platforms
Flutter:
Notes: Image by freepik

## Slide 43: Mobile Application
Two options are provided for selecting the image
Image is either selected from gallery or is captured through camera
Flutter provides image_picker package to access gallery or camera
Notes: Image by freepik

## Slide 44: Mobile Application
Network Model deployed on server connected through API
The first network takes the selected image and classifies it as retinal or non retinal image
If not retinal , another image is to be selected
Notes: Image by freepik

## Slide 45: Mobile Application
Network Model deployed on server connected through API
The first network takes the selected image and classifies it as retinal or non retinal image
If retinal, image is passed to second network
Notes: Image by freepik

## Slide 46: Mobile Application
Network Model deployed on server connected through API
The second network takes the retinal image and detects DR
Notes: Image by freepik

## Slide 47: Mobile Application
Network Model deployed on server connected through API
The second network takes the retinal image and detects DR
Notes: Image by freepik

## Slide 48: Web Application
Web application for the project is developed on React JS.
An open-source JavaScript library developed by Facebook
Enables the creation of highly responsive and interactive user interfaces
React JS:
Notes: Image by freepik

## Slide 49: Web Application
Already saved image can be selected
Browse for the image and select
S
S
S
Notes: Image by freepik

## Slide 50: Web Application
Already saved image can be selected
Browse for the image and select
S
S
S
Notes: Image by freepik

## Slide 51: Web Application
Already saved image can be selected
Browse for the image and select
S
S
S
Notes: Image by freepik

## Slide 52: Web Application
Network Model deployed on server connected through API
The first network takes the selected image and classifies it as retinal or non retinal image
If not retinal , another image is to be selected
If retinal, image is passed to second network
Notes: Image by freepik

## Slide 53: Web Application
Network Model deployed on server connected through API
The first network takes the selected image and classifies it as retinal or non retinal image
If not retinal , another image is to be selected
Notes: Image by freepik

## Slide 54: Web Application
Network Model deployed on server connected through API
The first network takes the selected image and classifies it as retinal or non retinal image
If not retinal , another image is to be selected
Notes: Image by freepik

## Slide 55: Web Application
Network Model deployed on server connected through API
The second network takes the retinal image and detects DR
Notes: Image by freepik

## Slide 56: Web Application
Network Model deployed on server connected through API
The second network takes the retinal image and detects DR
Notes: Image by freepik

## Slide 57: Web Application
Network Model deployed on server connected through API
The second network takes the retinal image and detects DR
Notes: Image by freepik

## Slide 58: Demonstration
Smartphone Application
Notes: Image by freepik

## Slide 59: Demonstration
Web Application
Notes: Image by freepik

## Slide 60: Demonstration
Web Application
Notes: Image by freepik

## Slide 61
Bibliography
Hehttps://www.cdc.gov/visionhealth/pdf/factsheet.pdf
Basit A, Fawwad A, Qureshi H NDSP Members, et al Prevalence of diabetes, pre-diabetes and associated risk factors: second National Diabetes Survey of Pakistan (NDSP), 2016–2017BMJ Open 2018;8:e020961. doi: 10.1136/bmjopen-2017-020961
Mohamed Akil, Yaroub Elloumi. Detection of retinal abnormalities using Smartphone-captured fundus images: A survey. Real-Time Image Processing and Deep Learning, Apr 2019, Baltimore, Maryland, United States. ff10.1117/12.2519094ff. ffhal-02121855f
Karakaya, M., Hacisoftaoglu, R.E. Comparison of smartphone-based retinal imaging systems for diabetic retinopathy detection using deep learning. BMC Bioinformatics 21 (Suppl 4), 259 (2020). https://doi.org/10.1186/s12859-020-03587-2
He, A., Li, T., Li, N., Wang, K. and Fu, H., 2020. CABNet: category attention block for imbalanced diabetic retinopathy grading. IEEE Transactions on Medical Imaging, 40(1), pp.143-153.
Kim, T.N., Aaberg, M.T., Li, P. et al. Comparison of automated and expert human grading of diabetic retinopathy using smartphone-based retinal photography. Eye 35, 334–342 (2021). https://doi.org/10.1038/s41433-020-0849-5
T. Li, Y. Gao, K. Wang, S. Guo, H. Liu, and H. Kang, “Diagnostic assessment of deep learning algorithms for diabetic retinopathy screening,” Inf. Sci., vol. 501, pp. 511–522, Oct. 2019
[8] Wang S, Zheng J, Hu HM, Li B. Naturalness preserved enhancement algorithm for non-uniform illumination images. IEEE Trans Image Process. 2013 Sep;22(9):3538-48. doi: 10.1109/TIP.2013.2261309. Epub 2013 May 2. PMID: 23661319.
[9] Zuiderveld, Karel J.. “Contrast Limited Adaptive Histogram Equalization.” Graphics gems (1994).

## Slide 62
Thank You
Notes: Image by freepik